Check serial number whether this instruction is needed or not.

# Hardware
## Disassemble the front case
Unscrew the 4 Torx screws as shown.
## Disassemble the LED board
Unscrew the black screw and separate the LED board from the front case.
## Disassemble the rear case
Unscrew the 4 Torx screws as shown.
## Remove 'C670' Chip Capacitor
Pull out the rear case very carefully to disassemble the main board from the body case. Remove 'C670' with a soldering iron. If necessary, the power board can be disassembled.
## Assemble sMS-200 cases
Repeat to assemble sMS-200 cases in the reverse order.
# Software
To change the micro SD card image, please refer to 'burn sdcard image' page.
## Windows
### Preparation
1. Download the new micro SD card image in the link below. Please be noted the image file is quite big (7.4GB BIN file) 20170112-RC6_V0.3.0.bin
2. Download the imageUSB utility and unzip.
3. Take out the micro SD card from the rear case of sMS-200 and insert to the USB port by using the micro SD card reader.
### Run imageUSB
Run imageUSB. The connected USB device will be shown up. If the connected USB device is not shown, click 'Refresh Drives'.
### Select an USB device
Select an USB device to write the new image file.
### Select the new image file
Click 'Browse' button and select the downloaded image file.
### Write the new image
Click 'Write' button to write the new image file to the micro SD card.
### Finish
1. Insert the micro SD card to the rear panel of sMS-200 again.
2. Power on sMS-200, and apply the latest software upgrade in Eunhasu animated GUI settings.
## macOS
### Preparation
1. Download the new micro SD card image in the link below. Please be noted the image file is quite big (7.4GB img file) 20170112-RC6_V0.3.0.dd.img
2. Download dd-utility from here or github. And install it.
3. Eject the micro SD card from the rear case of sMS-200 and insert to PC USB port by using the micro SD card reader.
### Start Restore
Click 'Restore' and select downloaded .img file.
Select SD card.
And start.
You can see progress.
After done, insert the SD card to sMS-200 rear.
You can also use command-line by terminal instead of dd utility. Refer to here.